Installing MAC Drivers

Installing the drivers for the MyBrewbot controller is pretty straight forward.

Click here to go to the Silicon Labs download page. Scroll down the list until you come to the Download for Macintosh OSX (v5) section. Here, click on the Mac OS X link to download the appropriate version for your machine.

Unzip the download and run the file SiLabsUSBDriverDisk 3.dmg. Click Agree, then the following window will be opened.

Continue through the various steps in the installer. Once it's complete, you may need to reboot your computer.

Now your MyBrewbot controller should be appearing when you connect it via USB. To check this, open a Terminal window and run the command ls /dev/cu.* and see if it appears on your list of devices.

NodeMCU PyFlasher

Download the NodeMCU PyFlasher from here: NodeMCU PyFlasher

NodeMCU PyFlasher doesn't have to be installed, just double-click it and it'll start.

- Enter the correct serial port for the controller. (Final step above)

- Browse to find the MyBrewbot_New.bin firmware included in the zip file.

- Set the baud rate to 115200

- Erase Flash? 

Decide whether you need to do a factory reset (clears wifi and all data) = Yes
or just a software update = No

- Hit the flash button and wait until the process is complete.

- Do a hard reset of the controller